## Slide 1
Arm imbalances in the TW-MZM model
Where they come from, what they do to EO bandwidth and eye, and how INTERCONNECT represents them

## Slide 2
The model: a familiar MZM, block by block
Same blocks, same names: the simple picture (left) is what INTERCONNECT simulates (right)
CWL_1 laser
SPLT_1 / SPLT_2 Y splitter / combiner
TW_1, TW_2 travelling-wave electrode, one per arm
OM_1, OM_2 phase modulator, one per arm
PHS_1 bias phase (quadrature)
PIN_1 photodetector
Reference device for every number: measured line 6NK0020 scaled to 16.5 mm · ng = 2.27 · Vπ = 4 V per arm · 100 Gb/s NRZ, 2 Vpp · balanced EO BW = 58.8 GHz

## Slide 3
Why only one imbalance can move the EO bandwidth
Each arm = an electrode filter H(f) × a constant weight. Weights change the volume, not the tone
Weights: loss, split, bias, Vπ, Y-loss
Act the same way on a slow bit and a fast bit → the whole curve shifts down, the normalised shape is identical → BW unchanged
Filter: group index ng
Sets how long light and RF stay in step. Different ng per arm → the two filters differ → the sum changes shape → BW moves

## Slide 4
1 Arm loss imbalance
One arm loses more light: the '0' no longer goes dark
Where it comes from
rough sidewall, particle or local defect in one arm
Where it enters the model
In INTERCONNECT
ATT_1
Optical Attenuator, arm 2
attenuation = ΔL (dB)
realistic: 0 – 0.3 dB
Why
EO BW: unchanged — light is dimmed by the same fraction at every frequency
Eye: fields no longer cancel at '0' → floor lifts, ER 14.6 → 12.0 dB at 3 dB

## Slide 5
2 Splitter imbalance
Light shared unequally between the arms: same signature as loss, but no light is lost
Where it comes from
Y-junction asymmetry: tip offset, unequal branches
Where it enters the model
In INTERCONNECT
SPLT_1
Waveguide Y Branch, input
coupling coefficient = 0.5 − ε
realistic: 50.5:49.5 – 52:48
Why
EO BW: unchanged — a constant amplitude ratio, frequency-flat
Eye: residual field at '0' → ER 14.6 → 8.4 dB at 80:20; mean power unchanged

## Slide 6
3 Static phase error
The interferometer is biased away from quadrature
Where it comes from
optical path difference between the arms
Where it enters the model
In INTERCONNECT
PHS_1
Optical Phase Shift (bias)
phase shift = 90° + φ
any value: nulled by the bias loop
Why
EO BW: unchanged — the bias only scales the slope (a weight)
Eye: levels sit asymmetrically on the cosine → crossing 50 → 24 % at 30°, eye closes near 60°

## Slide 7
4 Vπ imbalance
One arm is modulated less efficiently: fixable by re-setting the drive
Where it comes from
different gap or overlap per arm
Where it enters the model
In INTERCONNECT
OM_2
Optical Modulator, arm 2
phase coefficient × 1/(1+d)
realistic: d = 0.5 – 3 %
Why
EO BW: unchanged — both arms keep the same filter, only the weights differ
Eye: 2 Vpp falls short of max→min: ER 11.1 dB; drive re-set to 2.4 Vpp → 14.6 dB (= balanced)

## Slide 8
5 Group-index imbalance
The only imbalance that reshapes the frequency response
Where it comes from
different rib cross-section per arm
Where it enters the model
In INTERCONNECT
TW_1, TW_2
Traveling Wave Electrode × 2
optical index = ng(1 ± dn/2)
realistic: dn < 0.001
Why
EO BW: −0.03 GHz at dn = 0.001, −2.4 GHz at 0.01: grows as dn²
Eye: slightly more ISI: ER 14.6 → 14.1 dB even at dn = 0.02

## Slide 9
6 Y-branch excess loss
Common-mode: both arms lose the same fraction (not an imbalance)
Where it comes from
light scattered at the junctions
Where it enters the model
In INTERCONNECT
SPLT_1, SPLT_2
Waveguide Y Branch × 2
insertion loss = IL (dB)
realistic: 0.1 – 0.3 dB / branch
Why
EO BW: unchanged — same fraction lost at every frequency
Eye: whole eye scaled × 10−2IL/10: ER stays 14.6 dB; only the received power (and the noise-limited Q) drops

## Slide 10
From process errors to imbalances
Each process error is one row: compute its components once, enter each in its own block → no double counting
Process error | Arm loss | Split | Static phase | Vπ | ng | Y-loss
Waveguide ↔ electrode mask shift | — | — | — | ≈ 0 (symmetric) | — | —
Electrode gap error, one side | — | — | — | ● main | — | —
Rib width / etch depth error, one arm | ○ small | — | ● main | ○ small | ○ tiny | —
Y-junction asymmetry | — | ● main | ○ small | — | — | ○ small
Sidewall roughness / defect, one arm | ● main | — | ○ small | — | — | —
Temperature / stress gradient | — | — | ● main | — | — | —
Blunt junction tips (both) | — | — | — | — | — | ● main
Why a mask shift gives no Vπ imbalance
The field in each gap is symmetric about its centre. Both waveguides move off-centre by the same distance, one toward S and one away from it, so both see the same field.
No redundancy:
the six columns are six different physical quantities (amplitude, split, phase, efficiency, delay, common loss). One error can feed several columns, but each column receives each error only once.

## Slide 11
Real example: asymmetric over-etch + gap error + splitter
Realistic process errors: a large static phase (handled by the bias loop), everything else is small
Process error (arm 2) | Static phase | Vπ d | ng dn | Arm loss | Split
Rib 20 nm narrower, 10 nm deeper | 270 rad | 0.57 % | 5.2·10−4 | 0.036 dB | —
Electrode gap +0.1 µm (of 4.15) | — | 2.46 % | — | — | —
Y-junction 52 : 48 (typical) | — | — | — | — | ε = 0.02
Total entered in the model | bias loop → 0° | 3.03 % | 5.2·10−4 | 0.036 dB | ε = 0.02
270 rad = 43 × 2π: the arms' optical paths differ by tens of wavelengths, so the bias point is arbitrary from die to die → a bias loop is mandatory
-0.38 dB
eye ER
-0.01 GHz
EO bandwidth
-1.9 %
eye height
Mode solver: semi-vectorial FD, 550 nm film, 275 nm etch, 1 µm rib (ng = 2.26 vs 2.27 measured). RF field: thin-electrode conformal map. Arm loss assumes 0.3 dB/cm, all from sidewall scattering.

## Slide 12
Summary
Imbalance | EO bandwidth | Eye | Physical reason | INTERCONNECT
1 Arm loss | — | ER ↓ | '0' not dark: unequal fields | ATT_1 attenuation
2 Splitter | — | ER ↓, power kept | '0' not dark: unequal fields | SPLT_1 coupling coeff.
3 Static phase | — | leans, closes ~60° | off quadrature | PHS_1 phase shift
4 Vπ | — | ER ↓ at fixed drive | swing < max→min; re-set drive | OM_2 phase coefficient
5 Group index | ● ↓ ∝ dn² | slight ISI | arms filter differently | TW_1 / TW_2 optical index
6 Y-branch loss | — | scaled, ER kept | common-mode | SPLT_1, SPLT_2 insertion loss
Take-away
Only the group index can move the EO bandwidth, and realistic values do not. Process asymmetries show up mainly as a static phase (bias loop) and as small ER penalties (splitter, Vπ). All six are single, independent knobs in the GUI and in INTERCONNECT.